## Slide 1
Automated medical
equipment sorting
AR4 robot arm with computer vision and servo gripper
Scissors / Syringes / Tweezers

## Slide 2
Vision system
Intel RealSense D405
Wrist-mounted depth camera provides RGB + depth data at 30fps. Short-range design (7-50cm) is ideal for close tray scanning.
YOLOv8 object detection identifies scissors, syringes, and tweezers with bounding boxes and confidence scores.
Bounding box aspect ratio determines object orientation: wider than tall triggers a J6 rotation so the gripper can grab objects from any angle.
Camera
D405 depth
Detection
YOLOv8
Classes
3 instruments
Orientation
Auto-rotate J6

## Slide 3
Calibration and control
Custom calibration
E-stop based joint limit discovery replaces standard limit switches. J2/J3 single-direction calibration from seated position. Safe limits saved per session.
6 joints
calibrated
Camera-to-joint mapping
26+ calibration points map D405 camera coordinates to AR4 joint angles using linear regression. Overshoot correction compensates for systematic bias.
26+
calibration points
Safety system
Live joint limit checking from calibration file. Per-class gripper force. Safe waypoint routing through over_tray between every pick and place.
0.77°
avg J1 error

## Slide 4
System architecture
D405
camera
→
YOLOv8
detection
→
Linear
regression
→
AR4 arm
control
→
Servo
gripper
↓
Scissors bin
Syringes bin
Tweezers bin
Continuous loop: scan tray → detect objects → pick highest confidence → sort to bin → rescan until empty
Orientation detection via
bbox aspect ratio
Per-class grip force
(scissors: 135, tweezers: 140)

## Slide 5
Results and next steps
What works
Full pick-and-place from predetermined positions with gripper
YOLO detection of 3 medical instrument classes
Camera-to-joint calibration with linear regression (26+ points)
Automatic orientation detection and J6 rotation
Per-class gripper force and continuous scan-pick-sort loop
Custom safety system with live joint limit checking
Next steps
Polynomial regression for improved edge accuracy
Multi-object same-class support via spatial clustering
Permanent camera mounting solution
Limit switch repair for automated homing (J4/J5)
Expanded instrument classes
26+
Cal points
3
Object classes
6-DOF
Joint control
< 1°
J1 accuracy